Product technical card

| Product code | C20140303 |
| --- | --- |
| Category | 600 |
| Product type | Moulds for prefab concrete industrial building |
| Brand | / |
| Model | / |
| Year | 1980 |
| Technical characteristics | Nr.21 used moulds (construction years: the ’80s ) for the production of industrial buildings with double-shaped mild reinforcement beams, span up to 18-22 mt. Moulds are functioning and in not bad state of conservation. The ideal investment for companies interested in: - approaching this production branch with a minimal start-up engagement - realizing industrial buildings for their own real estate projects Full package comprises 21 steel moulds for producing plinths, columns, beams, roofslabs, floor; just moulds for walls are not included. In detail: nr.1 mould for 2-shaped beams (10-12%), span up to 18 22 mt nr.1 mould for columns 50x50, h=10 m, (including steps for bridge cranes) nr.1 mould for bridge-crane beams, H=1, span up to 10-12 mt nr.8 moulds for TT-shaped roof-slabs, span 8m, 2,4m wide, h=41 cm nr.4 moulds for TT-shaped roof-slabs, span 12-13m, 2,4m wide, h=41 cm nr. 2 mould for floors, span up to 16m, 2,4m wide, h=20-25 cm nr. 1 mould for foundation ring beams 30x40 nr. 1 mould for stairs nr. 2 moulds for hollow plinths 50x50 |
| Price: | on request |